## Slide 1: DoD-ADBI Collection and Shipment Training

## Slide 2: Training Overview: DoD-ADBI
Study Overview
Kit Review
Sample Collection and Processing
Sample Shipping
Sample Forms
NCRAD Website
Common Nonconformance Issues
Questions?

## Slide 3: DoD-ABDI Study Specimens
Timepoint | Plasma | Buffy Coat | RNA
All Visits | X | X | X
Biofluids Collection Schedule

## Slide 4: Kit Request Module
Website: kits.iu.edu/DOD-ADBI

## Slide 5: NCRAD Kit Request Module
Choose your site from the drop-down list.
The coordinator name and contact information will appear.
Verify that this information is accurate or correct it if necessary.

## Slide 6: DoD-ADBI Blood Kits
Indicate the quantity needed of each kit
**Note: You can order more than one type of kit in a single kit request**
1

## Slide 7: DoD-ADBI Blood Kits
Once selected, kit components with a picture of the chosen kit will appear at the bottom of the screen (Pictured)
Click “Submit” to turn in your request.

## Slide 8: DoD-ADBI Blood Kits Example Kit

## Slide 9: DoD-ADBI Supplemental Kits
Remember: Only one supplemental kit per year. If extra supplies are needed, order separately under the “Extra Supplies”.
Order here if extra supplies are needed.

## Slide 10: Specimen Labels

## Slide 11: Three Label Types
Kit Number
Collection Tube and Aliquot Label
Site ID/PID

## Slide 12: Kit Number Labels
Used to track patient samples and provide quality assurance – Will be placed on the following locations :
Blood Sample and Shipment Notification Forms
Cryoboxes that houses aliquots during shipping
One extra label provided
Provided by NCRAD in the kits

## Slide 13: Site ID Labels
Subjects will be identified by their DoD-ADBI PID
Sites will be responsible for handwriting this onto the provided labels
Must use Fine Point Marker
Each site will receive 3 markers in initial kit supply
Provided by NCRAD in the kits

## Slide 14: Collection Tube and Aliquot Label – Plasma and Buffy Coat
Only one label to be placed on ALL aliquot tubes
Collection Tube Label
Plasma Aliquot
  From EDTA tube sent to C2N and UPENN
Buffy Coat Aliquot
  From EDTA tube Sent to NCRAD
Collection Tube Plasma Aliquot

## Slide 15: Labeled EDTA (Purple-Top) Blood Collection Tube
Collection Tube/Aliquot Label
Site and PID Label

## Slide 16: Specimen Labels – Plasma and Buffy Coat
Specimen tube label only
Please place barcode near cap

## Slide 17: Labeling Biologic Samples
Please...
Label all collection and aliquot tubes before cooling, collecting, processing or freezing samples
Label only 1 subject’s tubes at a time to avoid mix-ups
Wrap the label around the tube horizontally. Label position is important for all tube types
Make sure the label is completely adhered by rolling between your fingers

## Slide 18: Handling/Processing Study Specimens

## Slide 19: Blood Draw Order
Draw Order | Collection Tube | Drawn At | Specimen Type | Aliquot Volume | Total Number of Aliquots | Shipping Destination | Shipping Temperature
1 | 3 EDTA (Purple-Top) Blood Collection Tubes (10 ml) | Each visit | Plasma | 1.8 ml | 1 | UPenn | Frozen
 |  |  | Plasma | 0.5 ml | Up to 26 | UPenn | Frozen
 |  |  | Buffy Coat | ~1.0 ml | Up to 3 | NCRAD | Frozen
2 | 1 PAXgeneTM Blood Collection Tube (2.5 ml) | Each visit | Whole Blood | N/A | N/A | NCRAD | Frozen
FASTING OVERNIGHT (MINIMUM 6 HOURS) IS REQUIRED FOR PLASMA SAMPLE COLLECTION. ONLY WATER IS PERMITTED UNTIL THESE BLOOD DRAWS ARE COMPLETED.

## Slide 20: Plasma Collection
Create up to 8 aliquots
Please Note: For DOD-ADBI there could be up to eight 0.5ml aliquots created per 10ml EDTA tube. Please refer to the blood process schematic.

## Slide 21: Plasma and Buffy Coat Preparation (10ml Lavender-Top Tube x 3)
Step One
Step Two
Step Three
Step Seven
Store tubes at room temp.
Check expiration date on collection tubes.
Label tubes with preprinted labels prior to blood draw.
Collect blood in EDTA Tubes allowing blood to flow for 10 seconds and ensuring blood flow has stopped.
Immediately after blood draw, invert tubes 8-10 times to mix samples.
Adhere preprinted labels to the yellow cryovial & purple cap cryovials.
First Aliquot 1.8 ml into yellow cryovial.
Aliquot 0.5 ml into each purple cryovial tube.
Store plasma aliquots at -80°C until shipment.
Adhere preprinted labels to the clear cap cryovials.
Using a clean pipette tip, collect the buffy coats (may have residual plasma and some RBCs included).
Transfer the buffy coats into the cryovial tubes.
Store buffy coat aliquots at -80°C until shipment.
Step Four
Step Five
Centrifuge samples at 1500 RCF (x g) at RT for 15 minutes.
Samples need to be spun, aliquoted, and in the freezer within 60 minutes from the time of collection.
Step Six
Pool all plasma from the 3 EDTA tubes into a 50ml conical tube and invert gently 3 times to mix the plasma.
Aliquot First 1.8ml
x 26

## Slide 22: Cryovial Cap Colors (Samples going to C2N & UPENN)
Purple Cryovial going to UPENN
Yellow Cryovial going to C2N
Remember: Plasma Aliquots (up to 27) per each study participant for shipment to UPENN. Up to 2 Study Participants per cryobox.

## Slide 23: Buffy Coat Collection

## Slide 24: Cryovial Cap Colors (Samples going to NCRAD)
Remember: Buffy Coats (3) per each study participant for shipment to NCRAD. Up to 3 Study Participants per cryobox
Clear Cryovial going to NCRAD

## Slide 25: RNA PAXgene™ Collection
Store tubes at room temp.
Check expiration date on collection tubes.
Label tubes with preprinted labels prior to blood draw.
Collect blood in PAXgeneTM tube allowing blood to flow for 10 seconds, and ensuring blood flow has stopped.
Immediately after blood draw, invert tube 8-10 times to mix sample.
Store tubes in wire rack at -80°C until shipment to NCRAD.
Do not store tube in Styrofoam racks.

## Slide 26: Sample Shipments to NCRAD

## Slide 27: Sample Shipments Summary

## Slide 28: Frozen Shipment Packaging
Samples shipped frozen to NCRAD
  Buffy Coat and PAXgeneTM
  Ship Monday-Wednesday Only
Hold packaged samples in a -80°C freezer until pickup.
Include copy of Blood Sample Shipment and Notification Form
Batch samples together
  6 participant samples or 2 cryoboxes with 3 participants each (Buffy Coat)
  Batch shipping should be performed quarterly or as a full shipment of specimens accumulates, whichever is sooner.

## Slide 29: Shipping Frozen Samples
Buffy Coats (3) Per each Study Participant
Up to 3 Study Participants per cryobox

## Slide 30: Frozen Shipment Packaging
Use the biohazard bag to package the (1) 25-Slot Cryobox and (3) Pax gene tubes in bubble sleeves.
Please make sure that all samples that are frozen and returned to NCRAD are in an upright position .
Cryovial box and Pax Gene Tubes in bubble sleeves placed in clear biohazard bag
(1) 25-Slot Cryobox
(3) Pax gene TM tubes in bubble sleeves.

## Slide 31: Frozen Shipping Packaging
Place 2-3 inches of dry ice in the bottom of the Styrofoam shipping container, then insert the cryoboxes laying upright.
Fully cover the cryoboxes with additional dry ice, and if possible, completely fill the shipper with pelleted dry ice.
Each Styrofoam shipper must contain about 10lbs (20 kg) of dry ice.

## Slide 32: Frozen Shipping – Dry Ice Requirements
Dry Ice label should not be covered with other stickers and must be completed or the shipping carrier will reject/return your package!
Net weight of dry ice in kg
5

## Slide 33: Blood Sample and Shipment Notification Form
A copy of the sample form must be emailed to NCRAD prior to the date of sample arrival.
Please include sample forms in all shipments of frozen.
Email: alzstudy@iu.edu

## Slide 34: NCRAD Blood Sample and Shipment Notification Form

## Slide 35: Sample Shipments to UPenn

## Slide 36: UPenn Frozen Shipment Packaging
Samples shipped frozen to UPenn
  Plasma
  Ship Monday-Wednesday Only
Hold packaged samples in a -80°C freezer until pickup.
Include copy of Blood Sample Shipment and Notification Form
NCRAD will include preprinted UPS return airbills for shipments to UPenn in the UPenn Frozen Shipping Kits.
Once the frozen shipment package is prepared, peel of the backing of the airbill and adhered the label onto the shipping box.
Please ensure that the UPS airbill sticker does not cover any of the warning labels (e.g. dry ice label or UN3373) or overlap taped seams.
Batch samples together
  4 study participant samples or 2 cryoboxes with 2 participants each (Plasma)

## Slide 37: UPenn Frozen Shipment Packaging
This is an image of the UPS return Airbill that will be provided by NCRAD. This label will be use by study sites to ship samples to UPenn. These labels are pre-made by the NCRAD team that includes the Study Site information as the sender and the ship to information as all UPenn’s information.
*Please note that all UPenn Frozen Shipping kits will include the UPS return airbill to ship to UPenn.*

## Slide 38: Shipping Frozen Samples
Plasma Aliquots (up to 27) per each study participant for shipment to UPENN. Up to 2 Study Participants per cryobox.

## Slide 39: UPenn Blood Sample and Shipment Notification Form

## Slide 40: Blood Sample and Shipment Notification Form
A copy of the sample form must be emailed to UPenn prior to the date of sample arrival.
Please include sample forms in all shipments of frozen.
Email Manifest to: Yang.Wan@pennmedicine.upenn.edu with “DoD ADBI” in the subject line in include the UPS tracking number.

## Slide 41: NCRAD Website Helpful Pages
https://ncrad.iu.edu/contact/friday-blood-draws
https://ncrad.iu.edu/contact/holiday-closures
Date | Holiday
January 1 | New Year’s Day
3rd Monday in January | Martin Luther King, Jr Day
4th Monday in May | Memorial Day
June 19 | Juneteenth
July 4 | Independence Day
1st Monday in September | Labor Day
4th Thursday in November | Thanksgiving
4th Friday in November | Friday after Thanksgiving
December 25 | Christmas Day

## Slide 42: Nonconformance Issues
Sample aliquots and collection tubes frozen at an angle/inverted
Fields left blank on Blood Sample and Shipment Notification Forms
    Last time participant ate often left blank/unknown
Incorrect data reported on Sample and Shipment Notification Forms
Multiple low volume aliquots
Recommendation:
Place aliquots in Argos boxes/tube rack in freezer upright until shipment
Recommendation: Complete Sample Notification forms during the participant study visit as samples are processed. If participant can not provide fasting info please write in N/A
Recommendation:
Lay out cryovials in a row and aliquot in order until plasma/buffy coat is depleted

## Slide 43: Nonconformance Cont.
Aliquots arriving to NCRAD without labels
Sample forms not faxed or scanned to NCRAD the day before shipment
Recommendation:
Ship Samples to NCRAD utilizing the Notification Form, by DoD-ADBI ID. Do not throw away labels until samples are packed and shipped.

## Slide 44: Contact Information
Questions?
  Ronae Williams
    Phone: (317) 278-9082
    E-mail: rdw2@iu.edu
  General NCRAD Contact
    Phone: (800) 526-2839
    E-mail: alzstudy@iu.edu
    Website: www.ncrad.iu.edu